## Slide 1: Emissions Events
John Cotton, Work Leader
Office of Compliance and Enforcement
Region 10 - Beaumont
Pratima Singh, Team Leader
Office of Compliance and Enforcement
Region 10 - Beaumont

## Slide 2: Presentation Outline
Emissions Events (EE): The Process
  Regulated Entity (RE) - Requirements
  TCEQ – Upset / Maintenance Level 3 (UML3) Investigation
  Situations – Common & Unique

## Slide 3: EEs, Why the Concern?
FY16 – Total Emissions 61,427,777 Pounds

## Slide 4: FY16 – 3,824 EEs

## Slide 5: Regulatory Basis
Texas State Implementation Plan
30 TAC Chapter 101 Subchapter F - Emissions Events and Scheduled Maintenance Startup, and Shutdown Activities

## Slide 6: EE Investigation Objectives
Protect public safety & health and property during the release
Prevention -- persistent problems are identified and corrected.
Consistency

## Slide 7: RE Requirements
Determine if an EE occurred
  Unauthorized Emissions
  Definitions
Recordable or Reportable?
  Reportable Quantities (RQ)
  On-site or STEERS Documentation
  24 Hour Notification Requirement
Final Record

## Slide 8: Emissions Event
Unauthorized emissions
  Upset
    Unplanned
    Unavoidable
    Breakdown or Excursion
  Common cause
or Unscheduled Maintenance, Startup, or Shutdown (MSS)
Notes: EE – Any upset event or unscheduled maintenance, startup, or shutdown activity, from a common cause that results in unauthorized emissions of air contaminants from one or more emissions points at a regulated entity.)

## Slide 9: Unauthorized emissions
Emissions of any air contaminant except water, nitrogen, ethane, noble gases, hydrogen, and oxygen that exceed any air emission limitation in a permit, rule, or order of the commission or as authorized by Texas Health and Safety Code.

## Slide 10: Maintenance/Startup/Shutdown
MSS
Unplanned
Scheduled
(101.211)
Unscheduled
(101.201)
Planned
Permitted
Notes: This is a simple diagram to help you visualize how the TCEQ rules and permitting and enforcement programs categorize MSS activities
See §101.222(c) for details

## Slide 11: Report or Record?
Released to Atmosphere ≥ Reportable Quantity (RQ) above Authorized Limit within 24 hour period
  Mixtures
  Boilers and Combustion Turbines
Notes: Pounds:
-40 CFR 302; 40 CFR 355; 30 TAC 101 or Default = 100
Mixture of air contaminants:
1-If proportions known, RQ for each compound applies
2-If proportions unknown for compounds with a named RQ, when the total mixture exceeds RQ for any one compound
3-Named RQs less than 0.02% of mixture and others les than 2% - total mixture RQ is 5,000 lbs.
4-5,000 lbs. for Natural gas (excluding CO2, water, nitrogen, methane, ethane, noble gases, hydrogen, oxygen) –or- crude oil emissions –or- 100 lbs. for associated H2S and mercaptans emissions
Boilers/combustion turbines: opacity is the only RQ that applies; 15% above limit, 6-min avg. Fuel = natural gas, coal, lignite, wood, fuel oil w/ HAPs concentration of less than 0.02% by weight
ED-approved reading from CEMS

## Slide 12: RQ Lists
40 CFR 302
40 CFR 355
30 TAC 101.1 (89)
Default = 100 lbs. (if not listed)

## Slide 13: Excess Opacity
Opacity at least 15 additional percentage points above a limit
Notes: Excess opacity - When an opacity reading is equal to or exceeds 15 additional percentage points above an applicable opacity limit, averaged over a six-minute period.
Opacity--The degree to which an emission of air contaminants obstructs the transmission of light expressed as the percentage of light obstructed as measured by an optical instrument or trained observer.
Note – the most stringent limit applies.

## Slide 14: Who
  Regulated Entity: defined in 30 TAC §101.1
    Location based
    Same owner / operator
    Pipelines are county-based
    Includes
      Regulated units
      Facilities
      Equipment
      Structures
      Sources
Notes: RE – who does this apply to?
§101.1 (86) Regulated entity--All regulated units, facilities, equipment, structures, or sources at one street address or location that are owned or operated by the same person. The term includes any property under common ownership or control identified in a permit or used in conjunction with the regulated activity at the same street address or location. Owners or operators of pipelines, gathering lines, and flowlines under common ownership or control in a particular county may be treated as a single regulated entity for purposes of assessment and regulation of emissions events.

## Slide 15: Reporting: STEERS
STEERS: State of Texas Environmental Electronic Reporting System
Emissions Events: use Air Emissions and Maintenance Events (AEME) module in STEERS

## Slide 16: STEERS Reporting Required
Except:
  Small businesses
    Less than 100 employees or less than $1 million in gross receipts
  When STEERS is down at the agency
  When reported under the Spill Rules
  (30 TAC Chapter 327)
Notes: The use of STEERS is encouraged except (obviously) when the program is unavailable.
Small business is define in Texas Government Code
"Small business" means a legal entity, including a corporation, partnership, or sole proprietorship, that: (A) is formed for the purpose of making a profit; (B) is independently owned and operated; and (C) has fewer than 100 employees or less than $1 million in annual gross receipts.

## Slide 17: Reporting: STEERS
When faxing an emissions event report:
  Use Form 10360, follow instructions
  Form can be found at:
  http://www.tceq.texas.gov/field/cefoumforms.html
  Recommend downloading and printing the form and instructions – having it available when your computer or internet connection fails.

## Slide 19: Initial Notification

## Slide 20: Initial Notification (cont’d)

## Slide 21: Final Report

## Slide 22: Final Report (cont’d)

## Slide 23: TCEQ Form 10360
https://www.tceq.texas.gov/assets/public/compliance/field_ops/fod_forms/upset/form_10360.pdf

## Slide 24: Where: TCEQ Regional Office

## Slide 25: Region FAX Numbers

## Slide 26: When, How & Where to Report an EE
TCEQ Guidance – Form 10360 https://www.tceq.texas.gov/assets/public/compliance/field_ops/fod_forms/upset/eefguide.pdf
Reportable Event/Activity Notification/Reporting Form https://www.tceq.texas.gov/assets/public/compliance/field_ops/fod_forms/upset/form_10360.pdf

## Slide 27: Maintaining Affirmative Defense Eligibility
Know RQs & Process Stream Composition
MSS reasonable / defendable estimates
If in doubt submit Initial Notification
Initial notification within 24 hours of discovery
Final Report within 14 days of event end
Be prepared with FAX as backup

## Slide 28: FAQ
Q: After I file my report, what happens.
A: Pratima will tell you.

## Slide 29: Emission Events Basics & Consistency
Pratima Singh
TCEQ Region 10
Air Program Team Leader

## Slide 30: The Initial Report
Submit the initial report via the State of Texas Environmental Electronic Reporting System (STEERS), within 24 hours of discovery of the event.
Meet the reporting requirements of 30 TAC 101.201(a).
Date and time of discovery, best know cause of the event, pollutants, emission point numbers, actions taken, etc.

## Slide 31: Initial Investigator Review
Verify the initial report meets the reporting requirements of 30 TAC 101.201(a)
Pollutants exceeding RQ, permits, permitted limits
Determine if an immediate on-site investigation is warranted based on possibly - citizen complaints, impact to immediate surrounding.

## Slide 32: The Final Report
Due two weeks after the end of the event.
Meet the reporting requirements of 30 TAC 101.201(b)
If a final is not submitted within two weeks after the end of the event, the initial becomes the final.
No final report for opacity events.
Include all pollutants from all emissions points as a result of the event.
The quantity value required to be reported is the quantity above zero, not the quantity above any applicable limit that may be imposed through rule or permit.

## Slide 33: Final Report Review
Verify that the report is a Reportable Emissions Event
Meets the reporting requirements of 30 TAC 101.201
Emissions must be speciated by compound descriptive type of all individually listed compounds or mixtures in RQ list 30 TAC § 101.1(89).
Evaluate emissions event for Affirmative Defense

## Slide 34: Example of Emissions Event

## Slide 35: Types
Oil & Gas
Petrochemical and General Industry
  Excessive Emissions Events
  Non-Excessive Emissions Events
  Excess Opacity Events
  Unplanned MSS Events

## Slide 36: Excessive Emissions Events
  Region decides if an emissions event is excessive based on the six criteria found in 30 TAC101.222(a)
    (a)(1) - Frequency of the facility’s emissions events – how and why. Past emissions events that occurred within one year prior to this event. Causes of previous incidents and whether the prior incidents were from a related cause and the overall time period that the events occurred.
    (a)(2) - Cause of emissions event – how and why. Malfunctioning equipment, poor maintenance, a scheduled activity that became an emissions event.

## Slide 37: Excessive Emissions Events
(a)(3) - the quantity and impact on human health or the environment of the emissions event. Any Federal or State standards that were exceeded, such as, NAAQS, MACT, NSPS, etc.; whether any ambient effects were documented from the emissions event including any modeling performed.
(a)(4) - Duration of the emissions event- duration based on the facility’s annual operating hours and the percentage of time the emissions event impacted the facility’s operating hours

## Slide 38: Excessive Emissions Events
(a)(5) - Percentage of the facility’s total annual operating hours during which emissions events occur - how and why -the percentage per facility identification number; if reviewing more than one emissions event, the percentage for all the events.
(a)(6) - Need for startup, shutdown, and maintenance activities- how and why -whether start up, shut down, or maintenance activities could have prevented the cause of one or more of the events.
The event is reviewed by the TCEQ EEE team. Includes modelling indicating impacts, and submittal of a Corrective Action Plan by the Regulated Entity.

## Slide 39: Non-Excessive Emissions events & Excess Opacity Events
Non-Excessive events - Conduct an affirmative defense review under 30 TAC §101.222(b-e).
Excess Opacity events - Conduct an affirmative defense review under 30 TAC §101.222(d-e).

## Slide 40: Unplanned MSS
Only planned MSS activities are authorized through the permitting process. Unplanned Maintenance, Startup, and Shutdown activities are unauthorized and will continue to be evaluated for an affirmative defense.
Conduct an affirmative defense review under 30 TAC §101.222(c).

## Slide 41: Fugitive Components & Heat Exchangers
Fugitive components may be the subject of an emissions event. Emissions from a fugitive component that are considered “leaks” are authorized under conditions of a permit or rules for leak detection and repair (LDAR). Emissions from a fugitive component not considered a leak under LDAR permit conditions or rules may be considered upset emissions and subject to the emissions events rules under 30 TAC Chapter 101.
Heat Exchanger Failures Resulting in an Emission Event - Like fugitive components, heat exchangers may suffer a catastrophic failure. When this occurs, the facility owner or operator will follow the requirements of 30 TAC Chapter 101, including claims for affirmative defense.

## Slide 42: Oil & Gas
The Railroad Commission of Texas (RRC) has primary regulatory jurisdiction over the oil and gas (O&G) industry. The TCEQ is the environmental agency for the state. The Memorandum of Understanding (MOU) between the RRC and TCEQ provides additional explanation of the agencies’ jurisdictions over various O&G activities. The MOU can be found in Title 16 Texas Administrative Code (TAC) §3.30

## Slide 43: Affirmative Defense
Depending on the type of Emissions Event, all of the relevant demonstration criteria in 30 TAC 101.222 have to be met to qualify for the Affirmative Defense.
As a basic principle, the commission uses the concept of good engineering and operating practices as a starting point to evaluate upsets. While this concept is still somewhat subjective, regulated industries and regulators have a range of experience that the commission believes make this standard interpretable and enforceable. The commission interprets good operating practices as those which use manufacturers' recommendations for equipment operation and maintenance, adequate training of operators, and any equipment modification.
The commission would interpret "beyond the control of the owner or operator" to include situations and events for which no standard operating procedure or training could be specifically devised.

## Slide 44: Violations
Violations documented may result either in a Notice of Violation or a Notice of Enforcement.
For emissions events that warrant formal enforcement (NOE), Prior to referral of an emissions event investigation for formal enforcement, the Regional Air Section Manager will send a Notice of Preliminary Emissions Event Finding to the RE. The letter will advise the RE that based on the information available, the TCEQ has determined that the emissions event meets the enforcement referral criteria and therefore intends to issue a NOE.

## Slide 45: Violations
The letter will advise the RE that within 10 business days of the date of the letter, the RE has the opportunity to contest the violation(s) documented in the Notice of Preliminary Event Finding. The letter requests that the RE submit any additional information that the TCEQ is unaware of and offers the RE the opportunity to schedule a meeting with agency staff.
Based on the information received, the region will make a determination on whether or not an NOE is warranted.

## Slide 46: NOE
Once the Notice of Enforcement has been issued, the TCEQ Enforcement Division handles the remainder of the processing.

## Slide 47: STEERS Expert Contacts
STEERS Questions: STEERS MC226 512-239-6925 steers@tceq.texas.gov | Physical Address TCEQ <Place Program Name and Mail Code Here> 12100 Park 35 Cir Austin, TX 78753 | Pesticide General Permit (EPR_PESTGP) WQ Processing Center MC140 512-239-BUGS (2847) PGP@tceq.texas.gov
Aggregate Production Operations (EPR_APO) WQ Processing Center MC140 512-239-APOP (2767) APO@tceq.texas.gov | Discharge Monitoring Report (eDMR/NetDMR) Enforcement Division MC224 512-239-eDMR (3367) netdmr@tceq.texas.gov | Petroleum Storage Tank (PST) PST Registration and Self-Certification MC138 512-239-2160
Air Emissions Maintenance Events (AEME) Field Operations MC 174 512-239-0416 | Emissions Banking and Trading (EBT) Questions: Emissions Banking and Trading Program, MC-206 512-239-4900 aqp@tceq.texas.gov | Pollution Prevention Planning (P2PLAN) Waste Reduction Policy Act Program MC108 512-239-3143 P2@tceq.texas.gov
Air New Source Review (EPR_NSR) Air Permits MC 163 512-239-1250 | Industrial and Hazardous Waste (IHW) Registration and Reporting MC 129 512-239-6413 | Public Drinking Water - Labs (PDWLAB) Public Drinking Water MC155 512-239-4691 PDWS@tceq.texas.gov
Annual Emissions Inventory Report (AEIR) Emissions Inventory, MC-164 512-239-1773 psinvent@tceq.texas.gov | Municipal Solid Waste (MSW) Municipal Solid Waste MC130 512-239-6700 elvi.yzaguirre@tceq.texas.gov | Public Drinking Water - Systems (PDWSYS) Public Drinking Water MC155 512-239-4691 PDWS@tceq.texas.gov
CAFO General Permit (EPR_CAFO) Applications Review & Processing MC 148 512-239-4671 CAFO@tceq.texas.gov | Municipal Solid Waste Registrations (EPR_MSW) Municipal Solid Waste Permits Section MC124 512-293-2334 | Storm Water General Permits (EPR_SW) Storm Water Processing Center MC228 512-239-3700 swpermit@tceq.texas.gov
Central Registry (CR) Questions: Central Registry Program MC 144 512-239-5175 registry@tceq.texas.gov | Occupational Licensing Computer Based Testing (CBT) Operator Licensing MC178 512-239-0176 | Training Roster Online Submittal (TROLS) Operator Licensing MC178 512-239-2262

## Slide 48: FAQ
Q: Once I report an EE in STEERS, am I done?
A: No, other reporting requirements may apply such as the emissions inventory (see 30 TAC §101.10) and deviation reporting (see 30 TAC 122). Also, create a final record of the event within two weeks.

## Slide 49: FAQ
Q: Do I only report unauthorized emissions?
A: No, report total emissions.

## Slide 50: FAQ
Q: How are non-reportable EE handled during Title V investigations?
A: A portion are reviewed against recordkeeping requirements and to ensure the event didn’t exceed an RQ.

## Slide 51: FAQ
Q: Are the only emission limits that apply to EE NSR lb/hr limits?
A: No, emission limits may be in permits, rules, or orders (see definition of unauthorized emissions in 30 TAC §101.1(108)).

## Slide 52: FAQ
Q: If an investigator determines an event met the affirmative defense criteria, can a violation be cited?
A: Yes. These criteria apply to agency enforcement actions. Violations may be cited for federal rules.

## Slide 53: FAQ
Q: What is the RQ for crude and natural gas?
A: For natural gas (excluding carbon dioxide, water, nitrogen, methane, ethane, noble gases, hydrogen, and oxygen) or air emissions from crude oil: 5,000 pounds or 100 pounds of hydrogen sulfide / mercaptans, whichever occurs first.

## Slide 54: FAQ
Q: Weather (heavy rains, high winds, drought or freeze, for example) caused an upset that that resulted in a reportable emissions event. Does the event meet the affirmative defense?
A: It depends, facilities should be designed and operated to withstand typical weather extremes for the area.

## Slide 55: FAQ
Q: A divestiture separated two production units into 2 companies that share a flare. Who reports emissions events when the flare is the EPN?
A: The company that holds the permit for the flare is responsible for reporting emissions from the EPN.

## Slide 56: FAQ
Q: The process flare was observed smoking. What documentation is required?
A: -- If the smoking event was due to an emissions event note that the flare was smoking as part of the recordable / reportable documentation. -- If the smoking was for more than 5 minutes in a 2-hour period estimate the quantities of air contaminates released and document accordingly.

## Slide 57: FAQ
Q: For pipelines, sites without a permit, or a site authorized by a PBR without an hourly limits required how is RQ calculated?
A: All emissions should be considered.

## Slide 58: Time for Your Questions